## Slide 1: Group 13
VDP1 Concept Designs

## Slide 2: Chassis and Skirt
Hovercraft Shape- There are two main hovercraft shapes that are predominantly used. Tear drop and rounded square shapes will most likely be the one we choose.
Size- Can only be 420 × 297mm in size. From one of side of the inflated craft to the other.
Reinforcement-The hovercraft needs to be light. If we make the body of the craft out of a single piece of light weight material it will likely bend and possibly break. To counter this a reinforcement layer could be added.
The are two main types of skirt.
Wall skirt- Easy to build, lighter, cheaper
Finger Skirt-Good at going over obstacles, good for high speeds, smoother ride.
Finger
Wall
Skirt
Body
Chassis Engineer - Bradley Blocksidge
Hovercraft lift
Momentum curtain- Higher pressure air under the hovercraft as less air leaked out the sides. Meaning the craft lifts higher. Open plenum- No added material so the craft will be lighter and the hovercraft will be easier to build.

## Slide 3: 1
All of the apparatus in this area should be symmetrical as much as possible to control the balance.
All of the dimensions should be measured for the balance test.
Payload Engineer – Xiang Zhang
There are two fans in 1 Both of the lift and propulsion are in the same size
Four small propulsion fans are in the corner of the hovercraft in 3
Easy to put the mass on
Help to control the balance when put the mass on
Two lifts and one propulsion are in 2
Two lift should be in the same size
Payload

## Slide 4: Turning of a Hovercraft
Requirements
A hovercraft of max size 297x420mm must be capable of completing a 180° turn within a minimum area of 1x1.2m.
The hovercraft needs to manoeuvre within a 2.4x1.2 meter area.
The hovercraft needs to be able to overcome obstacles of maximum height 5mm, if they can not be overcome by lift, the hovercraft needs to be able to avoid them through manoeuvers.
To Scale model of course
Obstacle Area
Turning area
Start/Finish
Hover Craft
Bow Thruster
Thrust fans can be turned off
Reduces affects from moment of inertia
Needs powerful lift fans
Additional Tubing
Harder to manufacture
More flexibility in design
Greater thrust
Expensive
More wires required
Uses up more power
Additional thrust fans
Liable to effects from moment of inertia
High radius of turn
More air redirected, smaller radius
Smaller radius requires more and better designed rudders
Works when coasting
Servomechanism rotating fan
More precise in angle of control
Control speed of rotation
Always needs thrust applied
More complex
Liable to effects from moment of inertia
Imprecise control
Integration Engineer - Paul Longe
Rudders

## Slide 5
Low in cost
Extra Energy
More Power
Less efficient
Less space requires
Low weight (plastic)
Low in cost
More thrust because of the length of blades
More efficient
More space requires
Low weight ( Carbon )
Low in cost
More thrust because of the length of blades
More efficient and power-full
More space requires
Low weight ( plastic )
Materials & Cost
Materials | Thickness | Cost
Aluminium sheet | 0.9mm | £11/m2
MDF | 3.6mm | £3/m2
Carbon Fiber | 0.75mm | £61.15/300mm x 300mm x 0.75mm
Craftfoam Blue | 25mm | £12/m2
For the main body of the hovercraft I would recommend Craftfoam Blue as it is very light material with Aluminium sheet in order not to brake from the load.
Rotors, Fans & Materials
Design Engineer – Alexandros Iakovos Agrafiotis

## Slide 6
BATTERY
● 2600mAh
● 28.8Wh
● 11.1V
● 5.2A
●Chargeable
Motion
Motor
Load
Motor
Other
servo motor
Stepper Motor
DC Linear
Actuator Motor
Brushless motor
Brushed motor
DC Geared Motor
Great torque, save space
High cost, low rotating speed
Produce heat, low efficiency,
low output power
Low energy cost, low electrical interference,
Stable, accurate and controllable rotate speed
Expensive
Cheap, stable rotate speed,
Cheap, Open-loop control
Comparatively expensive
Close-loop control, stability, high speed
change, steady torque
Small torque
Easy to control, direct force
on the liner direction
Expensive, hard to apply on motion control
Motors & Batteries
Powertrain Engineer – Keqi Shu
£8.90
£2.00
£21.71
£24.33
Very low
£19.99
z
Budget
Power
Weight
Stability

## Slide 7
Radio Transmitter
8 x 1.5V AA battery
(12V)
Li-Ion Battery
2600mAh, 11.1V
Receiver
6V input
Hovercraft
Electronic Speed Controller
Motor for Lift
Motor for Forward Thrust
Dual DC motor driver board
OR
The Hovercraft will need either 2 Electronics Speed Controllers, one for the Lift & one for Thrust (Total of £8) or a Dual DC motor driver board (£3.74+)
Specification: | Electronics Speed Controllers | Dual DC motor driver board
Control Speed | Pulse Width Modulation | Pulse Width Modulation
Brake | Yes | No
Low Voltage Protection Threshold | Yes | No
Over-heat protection: | Yes | No
Throttle signal loss protection | Yes | No
Electrical and Systems Engineer – Divine Abraham